Literature review

Topology optimization: talk about all the papers that Sigmund and other wrote

Methodology

Topology optimization

Topology optimization is an optimization technique that seeks to find the optimal shape within a volume that satisfies certain governing equations, while at the same time satisfying specific constraints. This technique is usually utilized for the design of structures with no preconceived shape. When topology optimization is used for this objective, the optimal shape is interpreted as material distribution within the specified volume, which is called the design domain. A classical application of topology optimization is the binary compliance problem, in which regions of solid and void materials are distributed in order to minimize the work done by external forces (this is called compliance), also subject to a volume constraint [1]. The mathematical formulation of this problem is as follows [2]:

min : c( bold{%rho} ) = bold{ f^T }bold{ u } newline s.t. : bold{ K(bold{%rho}) bold{u}} = bold{ f } newline V = sum from i in %OMEGA %rho_i v_i <= V_c newline 0 <= %rho_i <= 1 forall i in %OMEGA

In the above formulation, the design domain

This binary compliance problems suffers from a serious drawback; the problem is ill-posed and the solution will converge to a chattering solution, generating a checkerboard pattern with holes of infinitesimal size. To alleviate this, several restrictions must be made and the equations used to generate the volume must be

References

[1]	K. Liu and A. Tovar, “An efficient 3D topology optimization code written in Matlab,” Struct. Multidiscip. Optim., vol. 50, no. 6, pp. 1175–1196, Dec. 2014, doi: 10.1007/s00158-014-1107-x.
[2]	B. S. Lazarov and O. Sigmund, “Filters in topology optimization based on Helmholtz-type differential equations,” Int. J. Numer. Methods Eng., vol. 86, no. 6, pp. 765–781, 2011, doi: 10.1002/nme.3072.